## Slide 1: Assignment 6: Socket Communication
Prepared by: Adithyan M P

## Slide 2: Objective
Understand and document socket-based communication using AT commands.
Explore TCP/IP connectivity over cellular networks.
Study commands like AT+QIOPEN, AT+QISEND, AT+QICLOSE
Note: CelerSMS Emulator does not support these commands, so this is a theoretical assignment.

## Slide 3: What is Socket Communication?
A socket enables a device to send and receive data over a network.
TCP sockets are used for reliable connections, e.g., sending data to a web server.
LTE and GSM modules can use AT commands to create and manage sockets.

## Slide 4: Compatible Modules
Quectel EC25 (4G LTE)
SIM7600, BG96, SIM800 (2G/3G)
Modules must support TCP/IP stack and internet access.

## Slide 5: Common Socket AT Commands (Quectel EC25)
Command | Description
AT+CGDCONT=1,"IP","airtelgprs.com" | Set APN (PDP context)
AT+QIACT=1 | Activate PDP context
AT+QIOPEN=1,0,"TCP","example.com",80,0,1 | Open TCP connection
AT+QISEND=0,20 | Send data over socket
AT+QICLOSE=0 | Close socket

## Slide 6: Step-by-Step Socket Setup

## Slide 7: Expected Responses (Real Modem)
Command | Expected Response
AT+QIOPEN | +QIOPEN: 0,0 (success)
AT+QISEND | SEND OK
AT+QICLOSE | OK

## Slide 8: Emulator Limitation
CelerSMS AT Emulator only supports GSM SMS commands.
Commands like AT+QIOPEN and AT+QISEND return ERROR.
This assignment is completed via research and documentation.

## Slide 9: Applications in IoT
GPS trackers sending location to server.
Remote sensors uploading data to the cloud.
Smart meters reporting usage statistics.
Any M2M communication over cellular networks.

## Slide 10: Conclusion
Socket AT commands are critical for internet-based data transmission
Understanding socket communication helps build connected IoT systems.
Emulator testing not possible; use real hardware for full validation.